## Slide 1: Designing a 16-bit CPU
Jim Wright

## Slide 2: Standing on the shoulders of griants
Ben Eater https://eater.net/8bit
Review his site for concepts:
  Data Bus
  RAM
  Memory Access Register (MAR)
  Register
  Arithmetic Logic Unit (ALU)

## Slide 3: First things to decide
Data Bus
Address Bus
Instruction Size
Number of Micro-steps (we will talk about this in another class)

## Slide 4: Data Bus
The amount of data that can be moved around the system.
From RAM to Register
From ALU to Register/Memory
To Output Register (Ben’s CPU)

## Slide 5: Address Bus
The number of ‘slots’ in RAM
Size of MAR, size of Program Counter (PC)
Size of STACK

## Slide 6: Data Bus and Address Bus
Data Bus >= Address Bus the CPU can share the Data Bus
If the Data Bus < Address Bus, extra lines will be needed to the address bus
Can has two sperate busses, but planning is needed.

## Slide 7: Instruction Size
Number of bits in the instruction register.
Total number of instructions
Some CPUs use a complex masking scheme IIIISSDD

## Slide 8: Ben’s Computer
Data Bus: 8-bit
Address Bus: 4-bits
Instruction Size: 4-bits
Number of Micro-steps: 5 steps

## Slide 9: Ben’s Computer Instructions
0000 – NOP Do nothing
0001 – LDA Load reg A with RAM
0010 – ADD Add RAM to A put A
0011 – SUB Subtract RAM from A
0100 – STA Store Reg A to RAM
0101 – LDI Load 4 Low 4-bit to A
0110 – JMP Jump to Statement
0111 – JC Jump is Carry Flag set
1000 – JZ Jump is Zero Flag Set
1001 -
1010 -
1011 -
1100 -
1101 -
1110 – OUT Move A to Output
1111 – HALT Stop the Clock

## Slide 10: Ben’s Computer Instructions
NOP, OUT, HALT, Need top 4 bits
LDI, the data to move to A is in the low 4 bits.
JMP, JC, JZ, the address to jump to is the low 4 bits.
ADD, SUB, STA, the address to read is in low 4 bits.

## Slide 11: Ben’s Computer Instructions
Since both instructions and address are 4 bits, they fit into the data bus.
Small RAM and small instruction set.

## Slide 12: Ben’s Computer Sample Microstep
LDA
  Step 0, PC -> MAR
  Step 1, RAM -> IR, PC+
  Step 2, IR(low)->MAR,
  Step 3, RAM -> A Register

## Slide 13: Next Step up
The Motorola 6800 in 1974, 8-bit Data, 16-bit Address.
Intel 8008 in 1972, 8-bit Data, 14-bit Address
Data Bus: 8-bit, Address Bus: 8-bits is really old.

## Slide 14: Next Step up 8-bit 8-bit
Instruction set might as well be 8 bit to keep simple.